FILE ON EMBEDDED SYSTEMS LAB / ESCC303 / ON KEIL AND MULTISIM / DEPARTMENT OF ELECTRONIC SCIENCE / UNIVERSITY OF DELHI / By, / T Raja Aadhithan / 19/1031

TABLE OF CONTENTS
NO	EXPERIMENT	PAGE	SOFTWARE

1.1	Addition and subtraction using immediate addressing mode	3	KEIL
1.2	Addition and subtraction using register indirect addressing mode	4	KEIL
1.3	Addition and subtraction of two eight bit BCD numbers	5	KEIL
1.4	Multiplication using successive addition	6	KEIL
1.5	Multiplication and division using command.	7	KEIL

2	Multiplication of 16 bit numbers	8	KEIL
2.1	Hexadecimal number to BCD equivalent	11	KEIL
2.2	Hexadecimal number to ASCII equivalent	12	KEIL
2.3	Decimal number to Hexadecimal equivalent	13	KEIL

3.1	Sorting of ten 8-bits numbers in ascending order	14	KEIL
3.2	Sorting of ten 8-bits numbers in descending order	16	KEIL

4	Delay and Toggle port 1	18	KEIL

5.1	16 bit timer mode	19	KEIL
5.2	8 bit auto reload timer mode	20	KEIL

6	LED toggling	21	MULTISIM

7	Generating a Square Wave	22	MULTISIM

8	Seven segment Display	23	MULTISIM

9	LCD	26	MULTISIM

EXPERIMENT 1.1

Addition and subtraction of two eight bit hexadecimal numbers by immediate addressing mode and store the result in general purpose registers.

Code:

Output:

EXPERIMENT 1.2

Addition and subtraction of two eight bit hexadecimal numbers by register indirect addressing mode and store the result in scratch pad memory location.

Code:

Output:

EXPERIMENT 1.3

Addition and subtraction of two eight bit BCD numbers.

Code:

Output:

stored in R0

EXPERIMENT 1.4

Multiplication of two eight-bit hexadecimal numbers by successive addition.

Code:

Output:

THE OUTPUT IS FOUND AT R7,R6

EXPERIMENT 1.5

Multiplication of two eight-bit hexadecimal numbers using MUL command and division of two eight-bit hexadecimal numbers

Code:

MULTIPLICATION:

inputs: 40H , 41H
outputs: 43H , 44H

DIVISION:

inputs: 40H , 41H
outputs: 43H , 44H

Output:

EXPERIMENT 2
Multiplication of 16 bit numbers

Code:

FLOW CHART:
OUTPUT:

     The outputs are found at 50H to 53H registers

EXPERIMENT 2.1

Hexadecimal number to BCD equivalent

Code:

Output:

input: R0
output: R1 and R2

EXPERIMENT 2.2

Hexadecimal number to ASCII equivalent

Code:

Output:

EXPERIMENT 2.3

Decimal number to Hexadecimal equivalent
Code:

Outputs:
various values of inputs have been displayed:
port 0 is input and port 1 is output

DECIMAL HEX

99	63H

32	20H

02	02H

15	0FH

EXPERIMENT 3.1

 Sorting of ten 8-bits numbers stored in internal data memory in ascending order
Code:

Output:

Internal memory:

before running the code:

after running the code:

SFRs:

EXPERIMENT 3.2

 Sorting of ten 8-bits numbers stored in internal data memory in descending order
Code:

Output:

Internal memory:

before running the code:

after running the code:

SFRs:

EXPERIMENT 4

Write an assembly language program to generate the delay of X microseconds and toggle the Y bit of port 1. Using KEIL software.

EXPERIMENT 5.1

 Delay of 250 microseconds and toggle the bit P1.5 using 16 bit timer mode
Code:

Output:

The port toggles between these two states every 250us.

EXPERIMENT 5.2

 Delay of 4 seconds and toggle the bit P1.0 using 8 bit auto reload timer mode
Code:

Output:

TMOD REG:

The port toggles between these two states every 4 s.

EXPERIMENT 6
 Toggling two LEDS in such fashion when one is on the Another is off for equal time delay

Code:

Outputs:

EXPERIMENT 7
  Generating a square wave of bit P1.0 shown on oscilloscope.

Code:	Circuit:

Outputs:

EXPERIMENT 8
Seven segment display and 2x2 matrix keyboard

Code:

Theory:

Above, the button at B1 is held. As the scan progresses, it does the following:
1. Nothing is selected. Outputs A and B are both high, and we don't worry about inputs 1 and 2.
2. Column A is selected with a logical low.
  1. The system reads inputs 1 and 2. Both are open, so the pull-up resistors cause the inputs to be pulled high. Since this is an active low matrix, the high inputs indicate nothing is pressed.
3. The system deselects column A by driving it high and selects column B is by driving it low.
  1. The system reads inputs 1 and 2. Since switch B1 is held, the low level from the column selection shows up at input 1.
  2. By pairing the column output (B) with the detected switch (1), the system knows that switch B1 is pressed.
4. Finally, everything is deselected by driving both outputs high.

Circuit and Output:

EXPERIMENT 9
16x1 LCD DISPLAY

Code:

Theory:

16×1 LCD module is a very common type of LCD module that is used in 8051 based embedded projects. It consists of 16 rows and 1 column of 5×7 or 5×8 LCD dot matrices. The module were are talking about here is a type which is a very popular one . It is available in a 16 pin package with back light ,contrast adjustment function and each dot matrix has 5×8 dot resolution.

Circuit and Output: